10A NCAC 14J .1513	WALLS

Walls and partitions shall be made of either reinforced concrete or masonry or the following materials:

(1)	Steel grating of either tool-resisting steel or open hearth steel as specified in the plans:

(a)	Tool-resisting steel grating shall meet the following construction requirements:

(i)	Seven-eighths of an inch or one inch diameter vertical double-ribbed round bars spaced not over four inches on center, passing through and interlocking at each intersection with 3/8 inch x 2-1/4 inches or 3/8 inch x 2-1/2 inches tool-resisting flat bars spaced on 12 inch centers for 7/8 inch bars and on 18 inch centers for one inch bars;

(ii)	Vertical framing bars shall be 3/8 inch x 2-1/4 inches or 3/8 inch x 2-1/2 inches tool-resisting flat bars.

(b)	Open hearth steel grating shall meet the following construction requirements:

(i)	Seven-eighths of an inch or one inch diameter vertical double-ribbed round bars spaced not over four inches on center, passing through and interlocking at each intersection with 3/8 inch x 2-1/4 inches or 3/8 inch x 2-1/2 inches horizontal flat bars spaced on 12 inch centers for 7/8 inch bars and on 18 inch centers for one inch bars;

(ii)	Vertical framing bars shall be 3/8 inch x 2-1/4 inches or 3/8 inch x 2-1/2 inches open hearth flat bars.

(2)	Steel plate used in a wall or ceiling shall meet the following construction requirements:

(a)	not less than 3/16 inch open hearth steel, or

(b)	not less than 1/4 inch tool-resisting steel.

History Note:	Authority G.S. 153A-220; 153A-221;

Eff. June 1, 1990;

Pursuant to G.S. 150B-21.3A, rule is necessary without substantive public interest Eff. January 5, 2016.