10A NCAC 14J .1520	FOOD PASSES

(a)  The food pass in plate walls shall be approximately 12 inches wide x 4-1/2 inches high.  Hinged food pass shutters shall be about 13 inches wide and six inches high and they shall be made of 3/16 inch open-hearth steel plate.  The shutter shall form a shelf when in open position and it shall overlap the opening around the edges.

(b)  The food pass in grating walls shall be approximately 12 inches wide x 4-1/2 inches high, and a shelf 5 inches x 12 inches shall be riveted or welded to the bottom of the opening to facilitate the passage of food.

History Note:	Authority G.S. 153A-220; 153A-221;

Eff. June 1, 1990;

Pursuant to G.S. 150B-21.3A, rule is necessary without substantive public interest Eff. January 5, 2016.