10a NCAC 29c .0902	MONUMENTS

Permanent concrete monuments four inches in diameter or square, three feet long, shall be placed at not less than two corners of the subdivision provided that additional monuments shall be placed where necessary so that no point within the subdivision lies more than 500 feet from a monument. Two or more of the required monuments shall be designated as control corners. The top of each monument shall have an indented cross, metal pin, or metal plate to identify properly the location of the point. A monument shall be set at least 30 inches in the ground with at least six inches exposed above the ground unless this requirement is impractical because of traffic or other factors. All monuments shall be shown on the final plat.

History Note:	Authority G.S. 122-95; 143B-10;

Eff. March 21, 1980;

Pursuant to G.S. 150B-21.3A, rule is necessary without substantive public interest Eff. August 24, 2019.