11 NCAC 08 .1107	EXTERIOR

(a)  The home inspector shall inspect:

(1)	Wall cladding, flashings, and trim;

(2)	Entryway doors and a representative number of windows;

(3)	Garage door operators;

(4)	Decks, balconies, stoops, steps, areaways, porches, and appurtenant railings;

(5)	Eaves, soffits, and fascias;

(6)	Driveways, patios, walkways, and retaining walls; and

(7)	Vegetation, grading, and drainage with respect only to their effect on the condition of the building.

(b)  The home inspector shall:

(1)	Describe wall cladding materials;

(2)	Operate all entryway doors;

(3)	Operate garage doors manually or by using installed controls for any garage door operator;

(4)	Report whether or not any garage door operator will automatically reverse or stop when meeting reasonable resistance during closing; and

(5)	Probe exterior wood components where deterioration is suspected.

(c)  The home inspector is not required to inspect:

(1)	Storm windows, storm doors, screening, shutters, and awnings;

(2)	Fences;

(3)	For the presence of safety glazing in doors and windows;

(4)	Garage door operator remote control transmitters;

(5)	Geological conditions;

(6)	Soil conditions;

(7)	Recreational facilities (including spas, saunas, steam baths, swimming pools, tennis courts, playground equipment, and other exercise, entertainment, or athletic facilities), except as otherwise required in 11 NCAC 08 .1109(d)(5)(F);

(8)	Detached buildings or structures; or

(9)	For the presence or condition of buried fuel storage tanks.

History Note:	Authority G.S. 143-151.49;

Codifier determined that agency findings did not meet criteria for temporary rule Eff. October 15, 1996;

Temporary Adoption Eff. October 24, 1996;

Eff. July 1, 1998;

Amended Eff. February 1, 2007; April 1, 2005; July 1, 2000;

Readopted Eff. October 1, 2018.