15A NCAC 02B .0508	TESTS AND MEASUREMENTS APPLICABLE TO SICS

(a)  Determination of Type and Frequency of Tests and Measurements:

(1)	Introduction. The tables set forth in this Rule are designed to indicate, for any particular water pollution control facility or point source, the minimum standard tests and measurements that are to be performed, the minimum frequency with which the tests and measurements are to be conducted, and the location and minimum number of sampling points that are required.

(2)	Determination of Facility Class and SIC Numbers. Before the tables set forth in this Rule may be applied, the standard industrial classification(s) of the activities discharging to the water pollution control facility must be determined from The Standard Industrial Classification (SIC) Manual. The classification of the facility as determined by the Water Pollution Control System Operators Certification Commission, must also be known.

(b)  Modification of Test(s) or Measurement(s) Requirements:

(1)	If any of the tests and measurements, sampling points, or frequency of sampling requirements, as required in this Rule for a particular SIC group, are not applicable to the discharge of a particular water pollution control facility, or if it can be demonstrated that the objectives of this Section can be achieved by other acceptable means, then such requirements may be waived or modified to the extent that the Director determines to be appropriate.

(2)	In addition to the tests and measurements as listed in this Rule applicable to each of the SIC groups, persons subject to this Section may be required to perform such additional tests and measurements at such sampling points and with such frequency as are determined by the Director to be necessary to characterize constituents of the waste discharge and their effect upon the receiving waters. This monitoring may include but not be limited to weekends and holidays to ensure representative sampling and proper operation and maintenance of any facility.

(c)  Unclassified Activities:

(1)	Any person owning or operating a water pollution control facility who determines that a major SIC group(s) is not listed in this Rule for an activity subject to this Section shall so notify the Division.

(2)	The Director shall prescribe on a case-by-case basis the number and location of sampling points and the frequency with which tests and measurements must be made to characterize the quantity or quality of waste discharges resulting from any activity subject to this Section that is not included in the major SIC groups set forth in this Rule and to characterize the effects of the discharges upon the waters of this state.

(d)  Index of Major Standard Industrial Groups:

SIC Number		Major Products or Services

1400-1499		Mining

2000-2199		Food, Beverage and Tobacco Processing

2200-2299		Textile Processing

2400-2599		Lumber and Wood Products Except Wet Decking

2600-2699		Paper and Allied Products

2800-2899		Chemical and Allied Products

2900-2999		Petroleum Refining and Related Industries

3100-3199		Leather and Leather Products

3400-3699		Fabricated Metal Products Except Ordnance, Machinery and Transportation Equipment

Machinery Electrical Machinery, Equipment and Supplies

4900-4939		Electric, and Gas Services

4941			Water Supply

4952			Wastewater and all facilities discharging primarily domestic wastewater

7000-8999		Services

Abbreviations for sampling locations and frequencies to be used with SIC monitoring requirements:

"I" means influent "E" means effluent "U" means upstream "D" means downstream

"2/month" means samples are collected twice per month with a required 10 day interval between the collection of the samples

"3/week" means samples are collected three times per week on three separate days

MINING

MINIMUM REQUIREMENTS FOR SIC 1400-1499

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | Turbidity | E | Monthly | Monthly | Monthly | Monthly |
| 2. | Settleable Matter | E | Monthly | Monthly | Monthly | Monthly |
| 3. | TSS | E | Monthly | Monthly | Monthly | Monthly |
| 4. | pH | E | Monthly | Monthly | Monthly | Monthly |
| 5. | Toxics and Toxicity |  | ** | ** | ** | ** |

FOOD AND BEVERAGE PROCESSING AND TOBACCO PROCESSING

MINIMUM REQUIREMENTS FOR SIC 2000-2199

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 5. | Ammonia Nitrogen | E | Monthly | 2/month | Weekly | Weekly |
| 6. | Total Nitrogen | E | * | * | * | * |
| 7. | Total Phosphorus | E | * | * | * | * |
| 8. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, (C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 7. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 8. | Ammonia Nitrogen | E | 2/month | Weekly | 3/week | Daily |
| 9. | Total Nitrogen | E | * | * | * | * |
| 10. | Total Phosphorus | E | * | * | * | * |
| 11. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 12. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 13. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

TEXTILE PROCESSING

MINIMUM REQUIREMENTS FOR SIC 2200-2299

EFFLUENT LIMITED

| REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- |
|  |  | CLASS | CLASS | CLASS | CLASS |
|  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | COD | E | 2/month | Weekly | 3/week | Daily |
| 5. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 6. | Total Nitrogen | E | * | * | * | * |
| 7. | Total Phosphorus | E | * | * | * | * |
| 8. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  | CLASS | CLASS | CLASS | CLASS |
|  |  | I | II | III | IV |
| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, (C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 7. | COD | E | 2/month | Weekly | Weekly | Weekly |
| 8. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 9. | Total Nitrogen | E | * | * | * | * |
| 10. | Total Phosphorus | E | * | * | * | * |
| 11. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 12. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 13. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

LUMBER AND WOOD PRODUCTS (EXCLUDING WET DECKING)

MINIMUM REQUIREMENTS FOR SIC 2400-2599

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | COD | E | Monthly | 2/month | Weekly | 3/week |
| 5. | Total Phenols | E | 2/month | Weekly | 3/week | Daily |
| 6. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 7. | Total Nitrogen | E | * | * | * | * |
| 8. | Total Phosphorus | E | * | * | * | * |
| 9. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, 0C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, 0C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 200C | E | 2/month | Weekly | 3/week | Daily |
| 7. | COD | E | 2/month | Weekly | 3/week | Daily |
| 8. | Total Phenols | E | 2/month | Weekly | 3/week | Daily |
| 9. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 10. | Total Nitrogen | E | * | * | * | * |
| 11. | Total Phosphorus | E | * | * | * | * |
| 12. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 13. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 14. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

PAPER AND ALLIED PRODUCTS

MINIMUM REQUIREMENTS FOR SIC 2600-2699

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 5. | Total Nitrogen | E | * | * | * | * |
| 6. | Total Phosphorus | E | * | * | * | * |
| 7. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, (C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 7. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 8. | Total Nitrogen | E | * | * | * | * |
| 9. | Total Phosphorus | E | * | * | * | * |
| 10. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 11. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 12. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

CHEMICAL AND ALLIED PRODUCTS

MINIMUM REQUIREMENTS FOR SIC 2800-2899

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 5. | Total Nitrogen | E | * | * | * | * |
| 6. | Total Phosphorus | E | * | * | * | * |
| 7. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, (C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 7. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 8. | Total Nitrogen | E | * | * | * | * |
| 9. | Total Phosphorus | E | * | * | * | * |
| 10. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 11. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 12. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

PETROLEUM REFINING AND RELATED INDUSTRIES

MINIMUM REQUIREMENTS FOR SIC 2900-2999

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 5. | Total Phenols | E | 2/month | Weekly | 3/week | Daily |
| 6. | Oil and Grease | E | 2/month | Weekly | 3/week | Daily |
| 7. | Total Nitrogen | E | * | * | * | * |
| 8. | Total Phosphorus | E | * | * | * | * |
| 9. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, (C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 7. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 8. | Total Phenols | E | 2/month | Weekly | 3/week | Daily |
| 9. | Oil and Grease | E | 2/month | Weekly | 3/week | Daily |
| 10. | Total Nitrogen | E | * | * | * | * |
| 11. | Total Phosphorus | E | * | * | * | * |
| 12. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 13. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 14. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

LEATHER AND LEATHER PRODUCTS

MINIMUM REQUIREMENTS FOR SIC 3100-3199

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 5. | COD | E | 2/month | Weekly | Weekly | Daily |
| 6. | Ammonia Nitrogen | E | Monthly | Weekly | Weekly | Weekly |
| 7. | Oil and Grease | E | 2/month | Weekly | 3/week | Daily |
| 8. | Turbidity | E | Weekly | 3/week | Daily | Daily |
| 9. | Total Nitrogen | E | * | * | * | * |
| 10. | Total Phosphorus | E | * | * | * | * |
| 11. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, (C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 7. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 8. | COD | E | 2/month | Weekly | 3/week | Daily |
| 9. | Ammonia Nitrogen | E | 2/month | Weekly | 3/week | Daily |
| 10. | Oil and Grease | E | 2/month | Weekly | 3/week | Daily |
| 11. | Turbidity | E | Weekly | Weekly | 3/week | Daily |
| 12. | Total Nitrogen | E | * | * | * | * |
| 13. | Total Phosphorus | E | * | * | * | * |
| 14. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 15. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 16. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

FABRICATED METAL PRODUCTS EXCEPT ORDINANCE: MACHINERY AND TRANSPORTATION EQUIPMENT MACHINERYELECTRICAL MACHINERY, EQUIPMENT AND SUPPLIES

MINIMUM REQUIREMENTS FOR SIC 3400-3699

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | Oil and Grease | E | 2/month | Weekly | 3/week | Daily |
| 4. | Total Nitrogen | E | * | * | * | * |
| 5. | Total Phosphorus | E | * | * | * | * |
| 6. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 7. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | pH | E | Weekly | Weekly | 3/week | Daily |
| 3. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 4. | Oil and Grease | E | 2/month | Weekly | 3/week | Daily |
| 5. | Total Nitrogen | E | * | * | * | * |
| 6. | Total Phosphorus | E | * | * | * | * |
| 7. | Toxics and Toxicity |  | ** | ** | ** | ** |

ELECTRICAL AND GAS SERVICES

MINIMUM REQUIREMENTS FOR SIC 4900-4939

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | Weekly | Weekly |
| 2. | Temperature, (C | E | Weekly | Weekly | Weekly | Weekly |
| 3. | Total Nitrogen | E | * | * | * | * |
| 4. | Total Phosphorus | E | * | * | * | * |
| 5. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | Weekly | Weekly |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | pH | E | Weekly | Weekly | Weekly | Weekly |
| 3. | Temperature, (C | E | Weekly | Weekly | Weekly | Weekly |
| 4. | Total Nitrogen | E | * | * | * | * |
| 5. | Total Phosphorus | E | * | * | * | * |
| 6. | Toxics and Toxicity |  | ** | ** | ** | ** |

Note: The following monitoring for steam electric generating establishments discharging once through cooling water or cooling tower blowdown shall be required whether or not the discharge is from a classified facility.

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | Temperature, (C | E | Cont. | Cont. | Cont. | Cont. |
| 2. | Temperature, (C | U, D | 3/week+ | 3/week+ | 3/week+ | 3/week+ |
| 3. | Flow |  | Continuous | Continuous | Continuous | Continuous |
|  |  |  | during | during | during | during |
|  |  |  | discharge | discharge | discharge | discharge |

WATER SUPPLY PLANTS

MINIMUM REQUIREMENTS FOR SIC 4941

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | Settleable Solids | E | Weekly | Weekly | Weekly | Weekly |
| 2. | TSS | E | 2/month | 2/month | 2/month | 2/month |
| 3. | Turbidity | E | Weekly | Weekly | Weekly | Weekly |
| 4. | pH | E | Weekly | Weekly | Weekly | Weekly |
| 5. | Chloride | E | Weekly | Weekly | Weekly | Weekly |

DOMESTIC WASTEWATER AND OTHER FACILITIES DISCHARGING PRIMARILY DOMESTIC

MINIMUM REQUIREMENTS FOR SIC 4952

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | 2/month | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | I,E | 2/month | Weekly | 3/week | Daily |
| 4. | TSS | I,E | 2/month | Weekly | 3/week | Daily |
| 5. | Ammonia Nitrogen | E | Monthly | 2/month | Weekly | 3/week |
| 6. | Fecal Coliform | E | 2/month | Weekly | 3/week | Daily |
| 7. | Total Nitrogen | E | * | * | * | * |
| 8. | Total Phosphorus | E | * | * | * | * |
| 9. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | 2/month | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Daily | Daily | Daily | Daily |
| 5. | Temperature, (5 | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | I,E | 2/month | Weekly | 3/week | Daily |
| 7. | TSS | I,E | 2/month | Weekly | 3/week | Daily |
| 8. | Ammonia Nitrogen | E | 2/month | Weekly | 3/week | Daily |
| 9. | Residual Chlorine | E | 2/week | 2/week | 3/week | Daily |
| 10. | Fecal Coliform | E | 2/month | Weekly | 3/week | Daily |
| 11. | Fecal Coliform | U,D | 2/month | Weekly | 3/week+ | 3/week+ |
| 12. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 13. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 14. | Total Nitrogen | E | * | * | * | * |
| 15. | Total Phosphorus | E | * | * | * | * |
| 16. | Toxics and Toxicity |  | ** | ** | ** | ** |

SERVICES

MINIMUM REQUIREMENTS FOR SIC 7000-8999

EFFLUENT LIMITED

|  | REQUIRED TEST | LOCATION | FREQUENCY |
| --- | --- | --- | --- |
|  |  |  | CLASS | CLASS | CLASS | CLASS |
|  |  |  | I | II | III | IV |
| 1. | pH | E | Weekly | Weekly | 3/week | Daily |
| 2. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 3. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 4. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 5. | Ammonia Nitrogen | E | Monthly | 2/month | Weekly | 3/week |
| 6. | Detergents (MBAS) | E | 2/month | Weekly | 3/week | Daily |
| 7. | Fecal Coliform | E | 2/month | Weekly | 3/week | Daily |
| 8. | Total Nitrogen | E | * | * | * | * |
| 9. | Total Phosphorus | E | Monthly | 2/month | Weekly | 3/week |
| 10. | Toxics and Toxicity |  | ** | ** | ** | ** |

WATER QUALITY LIMITED

| 1. | Dissolved Oxygen | E | Weekly | Weekly | 3/week | Daily |
| --- | --- | --- | --- | --- | --- | --- |
| 2. | Dissolved Oxygen | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 3. | pH | E | Weekly | Weekly | 3/week | Daily |
| 4. | Temperature, (C | E | Weekly | Weekly | 3/week | Daily |
| 5. | Temperature, (C | U,D | Weekly | Weekly | 3/week+ | 3/week+ |
| 6. | BOD, 5-day, 20(C | E | 2/month | Weekly | 3/week | Daily |
| 7. | TSS | E | 2/month | Weekly | 3/week | Daily |
| 8. | Ammonia Nitrogen | E | Monthly | 2/month | Weekly | 3/week |
| 9. | Detergents (MBAS) | E | 2/month | Weekly | 3/week | Daily |
| 10. | Fecal Coliform | E | 2/month | Weekly | 3/week | Daily |
| 11. | Total Nitrogen | E | * | * | * | * |
| 12. | Total Phosphorus | E | * | * | * | * |
| 13. | Toxics and Toxicity |  | ** | ** | ** | ** |
| 14. | Conductivity | E | Weekly | Weekly | 3/week | Daily |
| 15. | Conductivity | U,D | Weekly | Weekly | 3/week+ | 3/week+ |

+ Upstream and Downstream monitoring in water quality limited waters is to be conducted three times per week during June, July, August, and September, and once per week during the rest of the year.

* Total Nitrogen and Phosphorus Monitoring

(1)	Monitoring Requirements

(A)	All facilities equal to or greater than 50,000 gpd, shall monitor for total N and P.

(B)	Facilities less than 50,000 gpd shall monitor for total N and P when discharging into nutrient sensitive waters as designated by the Division.

(2)	Monitoring frequency for total N and P is based on river subbasins in two separate areas of the state as follows:

(A)	Western area includes the French Broad, Broad, Savannah, New, Watauga, Little Tennessee, and Hiwassee:

Facility Design Capacity:					Frequency

(i)	50,000 gpd or higher					Semi-annually

(ii)	1,000,000 gpd or higher					Quarterly.

(B)	Piedmont and Eastern area includes the Catawba, Lumber, Yadkin, Cape Fear, Chowan, Neuse, Pasquotank, Roanoke, Tar-Pamlico, and White Oak:

Facility Design Capacity					Frequency

(i)	50,000 gpd or higher					Quarterly

(ii)	1,000,000 gpd or higher					Monthly.

(3)	Definition for Total Nitrogen and Total Phosphorus:

(A)	Total Nitrogen shall be the sum of total Kjeldahl nitrogen, nitrate nitrogen, and nitrite nitrogen expressed as "N" in milligrams per liter (mg/L).

(B)	Total Phosphorus shall include all orthophosphates and condensed phosphates, both dissolved and particulate, organic and inorganic, expressed as "P" in milligrams per liter (mg/L).

** Specific test type, conditions, and limitations shall be defined by permit. Toxicity limits shall be applied to all major discharges and all discharges of complex wastewater. Toxicity limitations and monitoring requirements may be applied to permits for other discharges when such discharge may impair the best use of the receiving water by the discharge of toxic substances in toxic amounts.

Specific frequency shall be defined by individual permit conditions. For most facilities with continuous and regularly occurring discharges, frequency will be defined as a minimum of quarterly.

History Note:	Authority G.S. 143-215.3(a)(1); 143-215.64; 143-215.65; 143-215.66;

Eff. February 1, 1976;

Amended Eff. April 1, 1993; December 1, 1984; November 1, 1978;

Readopted Eff. May 1, 2020.