15A NCAC 02C .0303	APPLICATION FOR PERMIT

A property owner or the property owner's agent shall submit an application for a permit to construct, repair, or abandon a private drinking water well to the local health department for the county where the well is located or will be located. The application shall include:

(1)	The name, the address, and the phone number of the proposed well property owner or agent;

(2)	The signature of owner or agent;

(3)	The address and the parcel identification number of the property where the proposed well is to be located;

(4)	A plat or site plan;

(5)	The intended use(s) of the property;

(6)	Other information deemed necessary by the local health department to determine the location of the property and any site characteristics, such as existing or permitted sewage disposal systems, easements or rights of way, existing wells or springs, surface water or designated wetlands, chemical or petroleum storage tanks, landfills, waste storage, known source of release of contamination, and any other characteristics or activities on the property or adjacent properties that could impact groundwater quality or suitability of the site for well construction;

(7)	Any current or pending restrictions regarding groundwater use as specified in G.S. 87-88(a); and

(8)	Any variances regarding well construction or location issued under 15A NCAC 02C .0118.

History Note:	Authority G.S. 87-87; 87-97;

Eff. July 1, 2008;

Readopted Eff. July 1, 2019.