15A NCAC 02D .0514	PARTICULATES FROM FERROUS JOBBING FOUNDRIES

Particulate emissions from any ferrous jobbing foundry cupola existing before January 2, 1972 shall not exceed:

Maximum Allowable

Process Weight		           Emission

In lb/hr			           Rate For Particulate In lb/hr

1,000					3.05

2,000					4.70

3,000					6.35

4,000					8.00

5,000					9.65

6,000					11.30

7,000					12.90

8,000					14.30

9,000					15.50

10,000					16.65

12,000					18.70

16,000					21.60

18,000					23.40

20,000					25.10

Any foundry existing before January 2, 1972, having a capacity greater than shown in the table and any new foundry, regardless of size, shall comply with the particulate emission limits pursuant to 15A NCAC 02D .0515(a).

History Note:	Authority G.S. 143-215.3(a)(1); 143-215.107(a)(5);

Eff. February 1, 1976;

Amended Eff. July 1, 1998; April 1, 1986; January 1, 1985;

Readopted Eff. November 1, 2020.