15A NCAC 02D .0544	PREVENTION OF SIGNIFICANT DETERIORATION Requirements FOR GreeNHouse GASES

(a)  The purpose of this Rule is to implement a program for the prevention of significant deterioration of air quality for greenhouse gases as required by 40 CFR 51.166. The minimum requirements described in the portions of 40 CFR 51.166 are hereby adopted as requirements under this Rule, except as otherwise provided in this Rule. Wherever the language of the portions of 40 CFR 51.166 adopted in this Rule speaks of the "plan," the requirements described therein shall apply to the source to which they pertain, except as otherwise provided in this Rule. Whenever the portions of 40 CFR 51.166 adopted in this Rule provide that the State plan may exempt or not apply certain requirements in certain circumstances, those exemptions and provisions of non-applicability are also hereby adopted under this Rule. However, this provision shall not be interpreted so as to limit information that may be requested from the owner or operator by the Director as specified in 40 CFR 51.166(n)(2). For purposes of greenhouse gases, the provisions of this Rule shall apply rather than the provisions in 15A NCAC 02D .0530. For all other regulated new source review (NSR) pollutants, the provisions in 15A NCAC 02D .0530 shall apply. A major stationary source or major modification shall not be required to obtain a prevention of significant deterioration (PSD) permit on the sole basis of its greenhouse gases emissions.

(b)  For the purposes of this Rule, the definitions contained in 40 CFR 51.166(b) and 40 CFR 51.301 shall apply except the definition of "baseline actual emissions." "Baseline actual emissions" means the rate of emissions, in tons per year, of a regulated NSR pollutant, as determined in accordance with Subparagraphs (1) through (3) of this Paragraph:

(1)	For an existing emissions unit, baseline actual emissions means the average rate, in tons per year, at which the emissions unit emitted the pollutant during any consecutive 24-month period selected by the owner or operator within the 5-year period preceding the date that a complete permit application is received by the Division for a permit required under this Rule. The Director shall allow a different time period, not to exceed 10 years preceding the date that a complete permit application is received by the Division, if the owner or operator demonstrates that it is more representative of normal source operation. For the purpose of determining baseline actual emissions, the following shall apply:

(A)	The average rate shall include fugitive emissions to the extent quantifiable, and emissions associated with startups, shutdowns, and malfunctions;

(B)	The average rate shall be adjusted downward to exclude any non-compliant emissions that occurred while the source was operating above any emission limitation that was legally enforceable during the consecutive 24-month period;

(C)	For an existing emission unit, other than an electric utility steam generating unit, the average rate shall be adjusted downward to exclude any emissions that would have exceeded an emission limitation with which the major stationary source shall currently comply. However, if the State has taken credit in an attainment demonstration or maintenance plan consistent with the requirements of 40 CFR 51.165(a)(3)(ii)(G) for an emission limitation that is part of a maximum achievable control technology standard that the Administrator proposed or promulgated under part 63 of the Code of Federal Regulations, the baseline actual emissions shall be adjusted to account for such emission reductions;

(D)	For an electric utility steam generating unit, the average rate shall be adjusted downward to reflect any emissions reductions under G.S. 143-215.107D and for which cost recovery is sought pursuant to G.S. 62-133.6;

(E)	For a regulated NSR pollutant, when a project involves multiple emissions units, only one consecutive 24-month period shall be used to determine the baseline actual emissions for all the emissions units being changed. A different consecutive 24-month period for each regulated NSR pollutant can be used for each regulated NSR pollutant; and

(F)	The average rate shall not be based on any consecutive 24-month period for which there is inadequate information for determining annual emissions, in tons per year, and for adjusting this amount if required by Parts (B) and (C) of this Subparagraph;

(2)	For a new emissions unit, the baseline actual emissions for purposes of determining the emissions increase that will result from the initial construction and operation of such unit shall equal zero; and thereafter, for all other purposes, shall equal the unit's potential to emit; and

(3)	For a plantwide applicability limit (PAL) for a stationary source, the baseline actual emissions shall be calculated for existing emissions units in accordance with the procedures contained in Subparagraph (1) of this Paragraph and for a new emissions unit in accordance with the procedures contained in Subparagraph (2) of this Paragraph.

(c)  In the definition of "net emissions increase," the reasonable period specified in 40 CFR 51.166(b)(3)(ii) shall be seven years.

(d)  In the definition of "subject to regulation", a greenhouse gas's global warming potential is the global warming potential published at Table A-1 of Subpart A of 40 CFR Part 98 and shall include subsequent amendments and editions.

(e)  The limitation specified in 40 CFR 51.166(b)(15)(ii) shall not apply.

(f)  Major stationary sources and major modifications shall comply with the requirements contained in 40 CFR 51.166(i) and (a)(7) and by extension in 40 CFR 51.166(j) through (r) and (w).

(g)  40 CFR 51.166(w)(10)(iv)(a) is changed to read: "If the emissions level calculated in accordance with Paragraph (w)(6) of this Section is equal to or greater than 80 percent of the PAL [plant wide applicability limit] level, the Director shall renew the PAL at the same level." 40 CFR 51.166(w)(10)(iv)(b) is not incorporated by reference.

(h)  15A NCAC 02Q .0102 is not applicable to any source to which this Rule applies. The owner or operator of the sources to which this Rule applies shall apply for and receive a permit as required in 15A NCAC 02Q .0300 or .0500.

(i)  When a particular source or modification becomes a major stationary source or major modification solely by virtue of a relaxation in any enforceable limitation that was established after August 7, 1980, on the capacity of the source or modification to emit a pollutant, such as a restriction on hours of operation, then the provisions of this Rule shall apply to the source or modification as though construction had not yet begun on the source or modification.

(j)  The provisions of 40 CFR 52.21(r)(2) regarding the period of validity of approval to construct are incorporated by reference except that the term "Administrator" is replaced with "Director".

(k)  Permits may be issued based on innovative control technology as set forth in 40 CFR 51.166(s)(1) if the requirements of 40 CFR 51.166(s)(2) have been met, subject to the condition of 40 CFR 51.166(s)(3), and with the allowance set forth in 40 CFR 51.166(s)(4).

(l)  A permit application subject to this Rule shall be processed in accordance with the procedures and requirements of 40 CFR 51.166(q). Within 30 days of receipt of the application, applicants shall be notified if the application is complete as to initial information submitted. Commencement of construction before full prevention of significant deterioration approval is obtained constitutes a violation of this Rule.

(m)  Approval of an application with regard to the requirements of this Rule shall not relieve the owner or operator of the responsibility to comply with applicable provisions of other rules of this Subchapter or 15A NCAC 02Q and any other requirements under local, State, or federal law.

(n)  In lieu of the requirements in 40 CFR 51.166(r)(6) and (7), this Paragraph shall apply. If the owner or operator of a source is using projected actual emissions to determine applicability with prevention of significant deterioration requirements, the owner or operator shall notify the Director of the modification before beginning actual construction. The notification shall include:

(1)	a description of the project;

(2)	identification of sources whose emissions could be affected by the project;

(3)	the calculated projected actual emissions and an explanation of how the projected actual emissions were calculated, including identification of emissions excluded by 40 CFR 51.166(b)(40)(ii)(c);

(4)	the calculated baseline actual emissions in Subparagraph (b)(1) of this Rule an explanation of how the baseline actual emissions were calculated; and

(5)	any netting calculations, if applicable.

If upon reviewing the notification, the Director finds that the project will require a prevention of significant deterioration evaluation, then the Director shall notify the owner or operator of his or her findings and the owner or operator shall not make the modification until a prevention of significant deterioration permit has been issued pursuant to this Rule. If the Director finds that the project will not require a prevention of significant deterioration evaluation and the projected actual emissions, calculated pursuant to 40 CFR 51.166(b)(40)(ii)(a) and (b), minus the baseline actual emissions, is 50 percent or greater of the amount that is a significant emissions increase, without reference to the amount that is a significant net emissions increase, for the regulated NSR pollutant, then, the Director shall require a permit application to include a permit condition for the monitoring, recordkeeping, and reporting of the annual emissions related to the project in tons per year, for 10 years following resumption of regular operations after the change if the project involves increasing the emissions unit's design capacity or its potential to emit for the regulated NSR pollutant; otherwise these records shall be maintained for five years following resumption of regular operations after the change. The owner or operator shall submit a report to the Director within 60 days after the end of each year during which these records must be generated. The report shall contain the items listed in 40 CFR 51.166(r)(6)(v)(a) through (c). The owner or operator shall make the information documented and maintained under this Paragraph available to the Director or the general public pursuant to the requirements in 40 CFR 70.4(b)(3)(viii). The monitoring, recordkeeping, and reporting requirements in this Paragraph shall not apply if the projected actual emissions, calculated pursuant to 40 CFR 51.166(b)(40)(ii)(a) and (b), minus the baseline actual emissions, is less than 50 percent of the amount that is a significant emissions increase, without reference to the amount that is a significant net emissions increase, for the regulated NSR pollutant.

(o)  Portions of the regulations in the Code of Federal Regulations (CFR) that are referred to in this Rule are incorporated by reference unless a specific reference states otherwise. The version of the CFR incorporated in this Rule, with respect to 40 CFR 51.166, is that as of July 1, 2019 at https://www.govinfo.gov/content/pkg/CFR-2019-title40-vol2/pdf/CFR-2019-title40-vol2-sec51-166.pdf and does not include any subsequent amendments or editions. Federal regulations referenced in 40 CFR 51.166 shall include subsequent amendments and editions. This Rule is applicable in accordance with 40 CFR 51.166(b)(48) and (b)(49)(iv) and (v). The publication may be accessed free of charge.

History Note:	Authority G.S. 143-215.3(a)(1); 143-215.107(a)(3); 143-215.107(a)(5); 143-215.107(a)(7); 143-215.108(b); 150B-21.6;

Eff. January 28, 2011 pursuant to E.O. 81, Beverly E. Perdue;

Pursuant to G.S. 150B-21.3(c), a bill was not ratified by the General Assembly to disapprove this rule;

Temporary Amendment Eff. December 23, 2011;

Amended Eff. July 1, 2012;

Temporary Amendment Eff. December 2, 2014;

Amended Eff. September 1, 2015;

Readopted Eff. November 1, 2020.