15A NCAC 02D .0611	MONITORING EMISSIONS FROM OTHER SOURCES

(a)  This Rule shall apply to sources of air pollutants, including toxic air pollutants, from sources that are not covered by 15A NCAC 02D .0606, .0607, .0608, or .0610(a).

(b)  The owner or operator of a source shall maintain records of production rates, throughputs, material usage, and other process operational information necessary to determine compliance with the facility's permit and all applicable requirements. The Director shall specify in the facility's permit, pursuant to 15A NCAC 02D .0605, the types of records that the owner or operator shall maintain.

(c)  If the records maintained under Paragraph (b) of this Rule are inadequate to determine compliance with the facility's permit and all applicable requirements, the Director may require the owner or operator to use monitoring instruments, and if monitoring instruments are necessary to demonstrate compliance with rules in Subchapters 02D or 02Q of this Chapter or with an emission standard or permit condition, the owner or operator of a source shall:

(1)	install, calibrate, operate, and maintain, in accordance with applicable performance specifications in 40 CFR Part 60 Appendix B, process and control equipment monitoring instruments or procedures necessary to demonstrate compliance with the emission standards in Subchapters 02D and 02Q of this Chapter;

(2)	comply with the requirements of 15A NCAC 02D .0613; and

(3)	maintain, in writing, data and reports of any monitoring instruments or procedures necessary to comply with Subparagraph (1) of this Paragraph that will document the compliance status of the sources or control equipment.

(d)  If monitoring instruments are necessary to demonstrate good operation and maintenance, the owner or operator of a source shall:

(1)	install, calibrate, operate, and maintain, in accordance with applicable performance specifications in 40 CFR Part 60 Appendix B, process and control equipment monitoring instruments or procedures necessary to demonstrate good operation and maintenance;

(2)	comply with the requirements of 15A NCAC 02D .0613 unless otherwise specified in any other applicable State rule or federal regulation, including 40 CFR Part 75 and 40 CFR 60.13. The Director shall determine that compliance with the quality assurance provisions of 40 CFR Part 51, Appendix P, is adequate if the data demonstrates that good operation and maintenance is being achieved; and

(3)	maintain, in writing, data and reports of any monitoring instruments or procedures necessary to comply with Subparagraph (1) of this Paragraph that will document that good operation and maintenance is being achieved.

History Note:	Authority G.S. 143-215.3(a)(1); 143-215.65; 143-215.66; 143-215.107(a)(4);

Eff. April 1, 1999;

Readopted Eff. November 1, 2019.