15A NCAC 02D .0935	FACTORY SURFACE COATING OF FLAT WOOD PANELING

(a)  For the purpose of this Rule, the following definitions shall apply:

(1)	"Flat wood paneling coatings" means wood paneling product that are any interior, exterior, or tileboard (class I hardboard) panel to which a protective, decorative, or functional material or layer has been applied.

(2)	"Hardboard" is a panel manufactured primarily from inter felted lignocellulosic fibers that are consolidated under heat and pressure in a hot-press.

(3)	"Tileboard" means a premium interior wall paneling product made of hardboard that is used in high moisture area or areas of the home.

(b)  This Rule applies to each flat wood paneling coatings source whose volatile organic compounds emissions meet the threshold established in 15A NCAC 02D .0902(b) at the facilities with flat wood paneling coating applications for the following products:

(1)	class II finishes on hardboard panels;

(2)	exterior siding;

(3)	natural finish hardwood plywood panels;

(4)	printed interior panels made of hardwood, plywood, and thin particleboard; and

(5)	tileboard made of hardboard.

(c)  Emissions of volatile organic compounds from any facility finished flat wood product operation subject to this Rule shall not exceed 2.1 pounds of volatile organic compounds per gallon material, excluding water and exempt compounds or 2.9 pounds of volatile organic compounds per gallon solids.

(d)  EPA Method 24 of Appendix A to 40 CFR Part 60 shall be used to determine the volatile organic compounds content of coating materials used at surface coating of flat wood paneling facilities, unless the facility maintains records to document the volatile organic compounds content of coating materials from the manufacturer.

(e)  Any facility meeting applicability requirements of Paragraph (b) of this Rule that has chosen to use add-on controls for flat wood paneling coating operation rather than the emission limits established in Paragraph (c) of this Rule shall install control equipment with an overall control efficiency of 90 percent or use a combination of coating and add-on control equipment on a flat wood paneling coating operation to meet limits established in Paragraph (c) of this Rule.

(f)  The owner or operator of any facility subject to this Rule shall comply with 15A NCAC 02D .0903 and .0958.

History Note:	Authority G.S. 143-215.3(a)(1); 143-215.107(a)(5);

Eff. July 1, 1980;

Amended Eff. September 1, 2010; July 1, 1996; December 1, 1989; January 1, 1985;

Readopted Eff. November 1, 2020.