15A ncac 02T .1108	SETBACKS

(a)  For residuals treatment and storage facilities, the following setbacks in feet shall be as follows:

Each habitable residence or place of assembly under

separate ownership or not to be maintained as part of the project site			100

Each private or public water supply source							100

Surface waters such as intermittent and perennial streams, perennial waterbodies, and wetlands	50

Each well with exception of monitoring wells						100

Each property line									50

(b)  For land onto which Class A bulk residuals are applied or stockpiled, the following setbacks in feet shall be as follows:

Liquid		Cake

Residuals	          Residuals

Each private or public water supply source					100		100

Surface waters such as intermittent and perennial streams, perennial

waterbodies, and wetlands						100		25

Surface water diversions such as ephemeral streams, waterways, and ditches	25		0

Groundwater lowering ditches where the bottom of the ditch intersects

the SHWT							25		0

Each well with exception of monitoring wells				100		100

Bedrock outcrops								25		0

(c)  For land onto which Class B residuals are applied or stockpiled, the following setbacks in feet shall be as follows:

Surface	Surface	Injection /

Application	Application	Incorporation

by Vehicle	by Irrigation

Each habitable residence or

place of assembly under separate ownership

or not to be maintained as part of the project site	400	400	200

Each habitable residence or place

of assembly owned by the permittee, the owner of

the land, or the lessee or operator of the land to be

maintained as part of the project site	0	200	0

Each property line	50	150	50

Public right of way	50	50	50

Each private or public water supply source	100	100	100

Surface waters such as intermittent and perennial streams,

perennial waterbodies, and wetlands 	32.8	32.8	32.8

Surface water diversions such as ephemeral streams, waterways,

and ditches	25	25	25

Groundwater lowering ditches where the bottom of the

ditch intersects the SHWT	25	100	25

Subsurface groundwater lowering drainage systems	0	100	0

Each well with exception of monitoring wells	100	100	100

Bedrock outcrops	25	25	25

Top of slope of embankments or cuts of two feet or more in

vertical height	15	15	15

Each building foundation or basement	0	15	0

Each water line	0	10	0

Nitrification field	0	20	0

(d)  For the construction and operation of surface disposal units, the following setbacks in feet shall be as follows:

Each habitable residence or place of assembly

under separate ownership or not to be maintained as part of the project site		400

Each property line									50

Public right of way									50

Each private or public water supply source							100

Surface waters such as intermittent and perennial streams, perennial waterbodies, and

Wetlands									100

Surface water diversions such as ephemeral streams, waterways, and ditches			25

Groundwater lowering ditches (where the bottom of the ditch intersects the SHWT)		100

Subsurface groundwater lowering drainage systems						100

Each well with exception of monitoring wells						100

Each water line										10

(e)  Setback waivers shall be written, notarized, signed by all parties involved, and recorded with the county Register of Deeds. Waivers involving the compliance boundary shall be in accordance with 15A NCAC 02L .0107.

(f)  Setbacks to property lines established in Paragraphs (a), (c), and (d) of this Rule shall not be applicable if the permittee, the entity from which the permittee is leasing, or the entity that executed the notarized landowner agreement in 15A NCAC 02T .1104(c)(4) owns both parcels separated by the property line.

(g)  Habitable residences or places of assembly under separate ownership constructed after the non-discharge facilities were originally permitted or subsequently modified are exempt from the setback requirements in Paragraphs (a) and (d) of this Rule.

History Note:	Authority G.S. 143-215.1; 143-215.3(a);

Eff. September 1, 2006;

Readopted Eff. September 1, 2018.