15A NCAC 02T .1506	SETBACKS

Remediation systems shall adhere to the following setbacks, unless greater setbacks are required to comply with minimum horizontal distance requirements set by the Division pursuant to 15A NCAC 02L .0107:

Feet

Any habitable residence or place of public assembly under separate ownership or not to

be maintained as part of the project site						100

Any well with the exception of a Division-approved groundwater monitoring

well										100

Surface waters (such as intermittent and perennial

streams, perennial waterbodies, and wetlands)						100

Surface water diversions (such as ephemeral streams, waterways, and ditches)			25

Groundwater lowering ditches (where the bottom of the ditch intersects the seasonal high

water table)									25

Subsurface groundwater-lowering drainage systems						25

Any building foundation except treatment facilities						15

Any basement										15

Any property line										50

Any water line										10

Any swimming pool									100

Rock outcrops										25

Public right-of-way									50

History Note:	Authority G.S. 143-215.1; 143-215.3(a);

Eff. September 1, 2006;

Readopted Eff. January 1, 2018.