SECTION .0600 - BULK DISTRIBUTION OF RECLAIMED WATER

15A NCAC 02U .0601	BULK DISTRIBUTION OF RECLAIMED WATER

(a)  Tank trucks and other equipment used to distribute reclaimed water shall be identified with advisory signs stating that they contain reclaimed water that is not intended for drinking.

(b)  Tank trucks used to transport reclaimed water shall not be used to transport potable water.

(c)  Tank trucks used to transport reclaimed water shall not be filled through on-board piping or removable hoses that may subsequently be used to fill potable water tanks.

(d)  The reclaimed water generator shall develop and maintain an education and approval program for all reclaimed water users.

(e)  The reclaimed water generator shall develop and maintain a record keeping program for bulk distribution of reclaimed water.

(f)  The reclaimed water generator shall develop and maintain a routine review and inspection program for reclaimed water users.

History Note:	Authority G.S. 143-215.1; 143-215.3(a);

Eff. June 18, 2011;

Readopted Eff. September 1, 2018.