15a ncac 18a .3613	camp buildings construction and maintenance requirements

All resident camp buildings shall be kept clean and in good repair and shall comply with the following specific requirements:

(1)	All floors shall be of such materials and so constructed to be easily cleanable, shall be kept free of obstacles to cleaning and shall be kept clean and in good repair. The floor area shall be sufficient to accommodate all necessary operations. Floors in dressing or locker rooms; laundry rooms; and toilet rooms shall be of non-absorbent materials such as sealed concrete, sealed wood, terrazzo, tile, durable grades of linoleum or plastic. In all rooms in which water is routinely discharged to the floor, or in which floors are subjected to flood-type cleaning, floors shall be sealed concrete, terrazzo, or tile and shall slope to drain and be provided with floor drains.

(2)	The walls of all rooms shall be kept clean and in good repair. All walls and ceilings in dressing or locker rooms; toilet rooms and bathrooms shall be easily cleanable; and walls shall have washable surfaces to the highest level reached by splash or spray in rooms or areas where such occur.

(3)	All rooms and areas shall be well lighted and ventilated, by natural or artificial means, which shall be effective under actual use conditions. Lighting fixtures and ventilation equipment shall be kept clean and in good repair.

History Note:	Authority G.S. 130A-235; 130A-248;

Eff. October 1, 2007;

Pursuant to G.S. 150B-21.3A, rule is necessary without substantive public interest Eff. July 20, 2019.