15A NCAC 18D .0203	RATING VALUES TO DETERMINE VARIOUS CLASSES OF CERTIFICATION

The designation of public water system treatment classifications shall be based on the following rating values:

PARAMETER						RATING VALUE

(1)	Surface Water Source

(a)	flowing stream						5

(b)	flowing stream with impoundment				7

(c)	raw water treatment					3

(2)	Ground Water Source

(a)	first five wells						5

(b)	add 1 point per 5 wells or fraction thereof over 5		1

(3)	Coagulation

(a)	aluminum sulfate, ferric chloride				10

(b)	polymer							5

(4)	Mixing

(a)	baffle							2

(b)	mechanical						4

(c)	air								3

(5)	Oxidation (pre-treatment)

(a)	C1202							5

(b)	ozone							5

(c)	KMn04							3

(d)	C12								3

(6)	Carbon Treatment						2

(7)	Aeration

(a)	mechanical draft						3

(b)	coke tray or splash tray					2

(c)	diffused							3

(d)	packed tower (VOC reduction)				10

(8)	pH Adjustment (primary)

(a)	caustic (NaOH)						10

(b)	lime or soda ash						3

(c)	acid								10

(9)	Sedimentation

(a)	standard rate						5

(b)	tube settlers						3

(c)	upflow							8

(d)	pulsators and plates					5

(10)	Contact Tank							1

(11)	Filtration

(a)	pressure

(i)	sand or anthracite					8

(ii)	synthetic media (birm)				8

(iii)	granular activated carbon (GAC)			9

(b)	gravity

(i)	sand						10

(ii)	anthracite (mixed) or GAC			12

(iii)	with surface wash or air scour			2

(c)	membrane						10

(12)	Ion Exchange

(a)	softener, Na cycle					5

(b)	softener, H cycle						7

(c)	Fe and Mn (greensand)					9

(d)	mixed bed or split stream					9

(13)	Lime Softening

(a)	spiractors						10

(b)	clarifier with coagulation					12

(c)	fuel burner (recarbonation)				5

(14)	Phosphate (sequestering agent)					5

(15)	Stabilization

(a)	acid feed						10

(b)	phosphate						2

(c)	caustic (NaOH)						10

(d)	lime or soda ash						3

(e)	contact units						5

(16)	Reverse Osmosis, Electrodialysis					15

(17)	Disinfection

(a)	gas C12							10

(b)	hypochlorite solution					7

(c)	C1202(sodium chlorite and C12)				13

(d)	ozone							13

(e)	ammonia and C12						12

(f)	ultraviolet light (uv)					5

(18)	Fluoridation

(a)	saturator							8

(b)	dry feed							8

(c)	solution (acid)						10

(19)	Pumping

(a)	raw								3

(b)	intermediate						1

(c)	finished							3

(d)	system booster						2

(20)	Storage

(a)	raw								1

(b)	treated ground level tank					1

(c)	elevated in system (each extra tank 1 point)			2

(d)	hydropneumatic						2

(21)	Population Served 1 point per 1,000 persons served			50 max

(22)	Plant Capacity 1 point per 1 MGD capacity				25 max

(23)	On-Site Quality Control

(a)	bacteriological

(i)	MPN/MF					5

(ii)	HPC						2

(iii)	MMO-MUG (Colilert)				2

(b)	pH

(i)	meter						2

(ii)	test kit						1

(c)	fluoride

(i)	meter						3

(ii)	colorimetric					3

(d)	chlorine

(i)	titrator						3

(ii)	colorimeter/spec.					2

(iii)	test kit						1

(e)	iron								1

(f)	hardness							1

(g)	alkalinity						1

(h)	turbidity							1

(i)	manganese						1

(j)	others (1 point each)					1

(k)	A.A. Spec, or G.C. Unit					5 each

History Note:	Authority G.S. 90A-21(c); 90A-22;

Eff. February 1, 1976;

Readopted Eff. March 1, 1979;

Amended Eff. August 1, 2000; August 3, 1992; January 1, 1992; September 1, 1990;

Readopted Eff. September 1, 2018.