15A NCAC 18E .1307	WASTEWATER SYSTEM ABANDONMENT

If a wastewater system is abandoned or is otherwise no longer in use, the tanks shall:

(1)	have the contents removed by a septage management firm permitted in accordance with G.S. 130A-291.1;

(2)	be removed, collapsed, or otherwise rendered unable to retain liquid, and backfilled; and

(3)	have the electrical components de-energized and above ground components removed.

History Note:	Authority G.S. 130A-335;

Eff. January 1, 2024.