21 NCAC 39 .1102	GENERAL REQUIREMENTS FOR EVALUATORS

In addition to the duties set forth in G.S. 130A-136.2, evaluators shall:

(1)	Provide a "notice of intent to construct" to the owner of a proposed wastewater system, so the owner can submit it to the local health department that has jurisdiction over the location of the proposed wastewater system;

(2)	Prepare a signed and sealed statement of special inspections that includes the following items:

(a)	The materials, systems, components, and work subject to special inspections and testing;

(b)	The type, frequency, and extent of each special inspection and each test;

(3)	Notify the owner if the system will require the owner to enter into a contract with a water pollution control system operator certified pursuant to Part 1 of Article 3 of Chapter 90A of the General Statutes; and

(4)	Maintain records for a period of seven years. This shall include a signed and dated copy of the operation and management program that was provided to the system owner and all inspection reports.

History Note:	Authority G.S. 130A-336.2;

Eff. June 1, 2021.